## Slide 1: Profiling and Performance Analysis
Keith Cok, SGI

## Slide 2: Profile and Performance Analysis
  Profiling points out code areas that take up most time
  Imperative for well balanced application
  Points out code and system bottlenecks
Notes: We are know at the point where we suspect the bottleneck is the application code, apart from the actual graphic calls themselves. I'd like to introduce a technique, called profiling, which let's us find the "hot spots" or areas of code that take up lots of time. Sometimes, this is intentional, for example, tight rendering loops, and other times the hot spots may point out poor code. It is almost always instructional, however, and can help you write code that is well balanced for a variety
of machines. At the very least, it will point out the system
bottlenecks.

## Slide 3: Two Methods of Software Profiling
Basic block
  a section of code that has one entry and one exit
  measures ideal time
Statistical sampling
  interrupts program execution and examines current location
  measures actual CPU cycles spent executing a line of code
Notes: There are two different kinds of profiling -- basic block measurements and statistical sampling. A basic block is a section of code that has one entry and one exit. Statistical sampling can be done either with the program counter or callstack. In each case, the system counts the amount of time spent either by tracking the basic block usage, or by
interrupting the execution of the program and examining either the call stack or program counter.
Basic block measure the ideal, or expected, time in each block of code. This can be misleading if cache misses are causing the hot spot. However, it is very useful for identifying code that repeats often.
Sampling, on the other hand, measures the actual time spent in a section of code. This will track the cache misses as well as measure the repetition. Comparing the basic block measurements to the sampling methods can be interesting. We'll see an example in just a moment.
It is important to note here that you must profile code that is
"complete". Optimizing profiled code with compiler flags can lead to erroneous results. Conversely, profiling debug code, or not compiler-flag optimized, can also produce misleading results.

## Slide 4: How Do You Profile Code?
  Compile/link with final compiler optimizations turned on
    cc foo.c -use_final_optimization_flags ....
  Instrument the code
    Unix: pixie foo.exe -> foo.exe.pixie
    Visual Studio: embedded in tool suite
  Run the application with relevant data sets
    foo.exe.pixie - args -> produces results data file
Notes: the mechanics of profiling code are easy to learn. First, compile your code with all the optimization flags turned on. it's fruitless to profile either debug code, or code which will change substantially if the compiler flags change.
Secondly, intrument the code. There is an explicit set of commands in UNIX to do this; on PC's, Visual studio will do this for you. Run the code with relevant data sets. This process creates a data file which is then examined.

## Slide 5: Profiling: Finding the Hot Spot
Function list, in descending order by exclusive ideal time
excl.% cum.% instructions calls function (dso: file, line)
[1] 10.3% 10.3% 190583064 11484 GL_CreateSurfaceLightmap (foo: gl_rsurf.c, 1293)
[2] 8.9% 19.2% 173920781 3203 S_Update_ (foo: snd_dma.c, 848)
[3] 8.2% 27.4% 145950460 338787 R_RenderBrushPoly (foo: gl_rsurf.c, 641)
[4] 5.9% 33.3% 97798122 1975976 __sin (libm.so: sin.c, 194)
[5] 4.1% 37.4% 82310479 240 GL_LoadTexture (foo: gl_draw.c, 990)
[6] 3.4% 40.8% 50786176 1204269 __glMgrim_Begin (libGLcore.so: mgras_prim.c, 221)
[7] 3.2% 44.0% 58099072 16797 R_DrawAliasModel (foo: gl_rmain.c, 232)
[8] 3.1% 47.1% 53832546 290970 R_RecursiveWorldNode (foo: gl_rsurf.c, 894)
[9] 3.1% 50.2% 43855299 437627 R_CullBox (foo: gl_rlight.c, 313; gl_rmain.c)
[10] 2.8% 53.0% 44666700 30981 EmitWaterPolys (foo: gl_warp.c, 187)
Notes: Here is what a results data file looks like:
series of functions along with the amount of time spent executing that function.
This data run comes from a very popular shoot-em-up video game that I ran for about 2-3 minutes. What can we learn from this?
The output is fairly typical: Note:
About 10 or so functions take up the majority of the time. Note the dropoff of individual function percentages.
GL_CreateSurfaceLightmap seems to be taking up the majority of the time.
The dma update function takes up a lot of time too. In another analysis that I ran (not shown here), the OpenGL wait for dma transfer was the leading function. Perhaps there is a way of speeding that up? is this an indication of a graphics bound application?
Note too, that the first system function call is sin. Perhaps one optimization might be to precalculate a sin table.
Also note that the first _graphics_ function call is down at number 6.

## Slide 6: Profiling: Fixing the Hot Spot
What do you look for?
  Common sub-expressions
  Loop invariant code
  Repeated pointer de-referencing
  Global variables and cache misses
  Unnecessary data movement
  ”Thin loops”
  ...
Notes: So, now you've profiled the code and found some offending functions. What's next? Look at the source code and find the bad code. Here are some things to look for:
blah blah blah.
Note that the compiler may otimize this for you. But the compiler is limited especially when function calls may be involved.
format of the course is to promote thought -- so sit back, listen think and then ....

## Slide 7: Profiling Example
// Code the old way
19: void old_loop() {
20: sum = 0;
21: for (i = 0;i < NUM; i++)
22: sum += x[i];
23: printf("sum = %f\n",sum);
24: }
Notes: consider the example on the screen. On the left you have old_loop and on the right there is new_loop. both functions do the same thing: add the contents of an array x.
New_loop is an improved function from application tuning. let's find out why it is faster.
Notice that old_loop is one large loop and nothing else. If you unroll the loop (and we'll talk more about that later), it will look like new_loop. After reprofiling the two functions, let's look at the analysis.

## Slide 8: Profiling Example: Profile Results
Line list, in descending order by time
------------------------------------------------------
cycles invocations function (dso: file, line)
4096 1024 old_loop sum += x[i];
2061 1024 old_loop for (i = 0;i < NUM; i++)
Notes: Here we see from the results file, that old_loop took 6160 cycles to complete. new_loop, on the other hand, took 4625 cycles.

## Slide 9: Profiling Example
// Code the old way // Code the new way
19: void old_loop() { 27: void new_loop () {
20: sum = 0; 28: sum = 0;
21: for (i = 0;i < NUM; i++) 29: ii = NUM%4;
22: sum += x[i]; 30: for (i=0; i < ii; i++)
23: printf("sum = %f\n",sum); 31: sum +=x[I];
24: } 32: for (i = ii; i < NUM; i +=4) {
33: sum += x[i];
34: sum += x[i+1];
35: sum += x[i+2];
36: sum += x[i+3];
37: }
38: printf(“ sum = %f\n”,sum);
39: }
Notes: consider the example on the screen. On the left you have old_loop and on the right there is new_loop. both functions do the same thing: add the contents of an array x.
New_loop is an improved function from application tuning. let's find out why it is faster.
Notice that old_loop is one large loop and nothing else. If you unroll the loop (and we'll talk more about that later), it will look like new_loop. After reprofiling the two functions, let's look at the analysis.

## Slide 10: Profiling Example: Profile Results
Old_loop:
cycles instructions calls function (dso: file: line)
[1] 6160 6168 1 old_loop (blahdso.so: blahdso.c, 19)
[2] 4869 8714 1 setup_data (blahdso.so: blahdso.c, 11)
New_loop:
[1] 4869 8714 1 setup_data (blahdso.so: blahdso.c, 11)
[2] 4625 4891 1 new_loop (blahdso.so: blahdso.c, 27)
Notes: Here we see from the results file, that old_loop took 6160 cycles to complete. new_loop, on the other hand, took 4625 cycles.

## Slide 11: Profile Example: Line Analysis
Line list, in descending order by time
------------------------------------------------------
cycles invocations function (dso: file, line)
4096 1024 old_loop sum += x[i];
2061 1024 old_loop for (i = 0;i < NUM; i++)
978 256 new_loop sum += x[i+3];
968 256 new_loop sum += x[i+2];
968 256 new_loop sum += x[i+1];
968 256 new_loop sum += x[i];
733 256 new_loop for (i = ii; i < NUM; i +=4)
7 1 new_loop ii = NUM%4;
Notes: Further analysis lets us take a look at the cost of each line of code. In this chart we can see the relative expense of old_loop and new_loop's main loop. We can easily tell that new_loop is a clear win over old_loop and precisely where the savings are.

## Slide 12: Profile and Performance Analysis
Profile Example: Visual C++/Intel
Function Percent of Hit Function
Time(s) Run Time Count
------------------------------------------------------------------
0.410 39.4 1 _old_loop
0.249 23.9 1 _new_loop
Notes: The preceding example was analyzed on SGI IRX. But what about other platforms? Will they also provide a savings? this chart gives the same analysis, but on a wintel platform using Visual C++.
With the IRIX example, the savings came out to be about 75% of the original cost. Here on this Intel platform, the savings was about 60%.

## Slide 13: Statistical vs. Basic Block Profile
Statistical vs. Basic block Profile
void ijk_loop(){ // loops kji and ikj as well
sum = 0;
for (i=0;i<XNUM;i++)
for (j=0;j<YNUM;j++)
for (k=0;k<ZNUM;k++)
sum += y[i][j][k];
}
printf("sum = %f\n",sum);
Notes: Earlier, I mentioned that ideal time was measured by basic block profiling. Memory latency can be measured by a sampling method. Let's take a look at an example.
This code is a 3d array and we are going to sum the values. It comes directly from a 3d texturing algorithm for an Oil & Gas application, so it's not completely contrived.
note the loop order is ijk. We have two other loops, not on the chart. Their ordering is kji and ikj. we';re going to examine which ordering is the most efficient.

## Slide 14: Basic Block vs. Statistical Sampling
Basic Block:
Percent cycles inst calls function
[1] 25.3% 51141434 37101028 1 ijk_loop foo.c, 47
[2] 25.3% 51141434 37101028 1 kji_loop foo.c, 57
[3] 25.3% 51141434 37101028 1 ikj_loop foo.c, 66
Statistical Sampling:
Percent Samples Procedure Function
[1] 38.0% 2700 kji_loop foo.c, 57
[2] 23.9% 1700 setup_data foo.c, 15
[3] 19.7% 1400 ikj_loop foo.c, 66
[4] 18.3% 1300 ijk_loop foo.c, 47
Notes: If we look at the basic block time -- that is the ideal time -- for each function, we see that they all take the same amount of time. You'd expect that as they do identical things.
however, if you glance at the output from the PC sampling run, you'll see something different. Note that the kji ordering takes about 38 percent of the total time. ikj takes about 20% almost the same as ijk's time of 18.3%
This example demonstrates the importance of using both types of profiling. both methods should be used to get a balanced picture of how welll the code runs.

## Slide 15: Now We Know About Hot Spots...
What do we do next?
  Use compilers to fine-tune code
  Use knowledge of language to optimize
  Hand-tune code
Profiling is fun, hard, and iterative…. And it can be highly effective